## Slide 1: FlowRadar: A Better NetFlow For Data Centers
Yuliang Li
Rui Miao Changhoon Kim Minlan Yu

## Slide 2: Flow coverage in data centers
Flow coverage
  Traffic monitoring needs to cover all the flows
Transient loop/blackhole
Fine-grained traffic analysis
Chart: Size (Byte)
| 1.0 | 10.0 | 100.0 | 1000.0 | 10000.0
Y-Value 1 | 0.02 | 0.1 | 0.5 | 0.3 | 0.08

## Slide 3: Temporal coverage in data centers
Temporal coverage
  Traffic monitoring needs millisecond-level flow information
Chart: Time (ms)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0
Y-Value 1 | 2 | 5 | 3 | 4 | 1 | 0 | 2 | 3
Short-time scale Loss rate
Timely attack detection
DoS

## Slide 4: Key insight: division of labor
Goal: report counters for all flows in fine-grained time granularity
Overhead at
the collector
Overhead at the switches
NetFlow
Mirroring
Limited per-packet processing time
Limited memory (10s of MB)
Collector has limited bandwidth and storage
Needs sampling

## Slide 5: Key insight: division of labor
Goal: report counters for all flows in fine-grained time granularity
FlowRadar
Use fixed operations per-pkt in switch
Overhead at
the collector
Overhead at the switches
NetFlow
Mirroring
Keep the memory usage small

## Slide 6: FlowRadar architecture
Correlate network-wide info to extract per-flow counter
Collector
Network
Analyze
Flow&counter
Each switch maintains a fast and efficient data structure for half-baked per-flow counter
Periodic report

## Slide 7: Challenge: handling collision?
Handling hash collision is hard
  Large hash table  high memory usage
  Linked list/Cuckoo hashing multiple, non-constant memory accesses
Flow | a | b |  |  | c
PacketCount | … | … |  |  | …
Flow d
d
1
collision

## Slide 8: Switch embraces collisions!
Handling hash collision is hard
  Large hash table  high memory usage
  Linked list/Cuckoo hashing multiple, non-constant memory accesses
Embrace the collision
    Less memory and constant #accesses

## Slide 9: Switch embraces collisions!
FlowXor |  |  |  |  |  | 
FlowCount |  |  |  |  |  | 
PacketCount |  |  |  |  |  | 
Embrace the collision: xor up all the flows
    Less memory and constant #accesses
FlowXor | a | a⊕b | b⊕c | b⊕c | a | c
FlowCount | 1 | 2 | 2 | 2 | 1 | 1
PacketCount | S(a) | S(a)+S(b) | S(b)+S(c) | S(b)+S(c) | S(a) | S(c)
Counting table
flow a: S(a)
Flow b: S(b)
Flow c: S(c)
a
a
b
b
c
c
[Invertible Bloom Lookup Table
(arXiv 2011)]
S(x): #packets in x

## Slide 10: Switch embraces collisions!
Counting table
1. Check and update the flow filter
2. Update counting table
  Packet from a new flow, update all fields
  Subsequent packets update only PacketCount
bloom filter: identify new flow
FlowXor | a | a⊕b | b⊕c | b⊕c | a | c
FlowCount | 1 | 2 | 2 | 2 | 1 | 1
PacketCount | S(a) | S(a)+S(b) | S(b)+S(c) | S(b)+S(c) | S(a) | S(c)
+1
+1
+1
d
⊕d
⊕d
⊕d
+1
+1
+1
+1
+1
+1
d
Flow filter
[Invertible Bloom Lookup Table
(arXiv 2011)]
Encoded flowset

## Slide 11: Easy to implement in merchant silicon
Switch data plane
  Fixed operations in hardware
  Small memory, 2.36MB for 100K flows
Switch control plane
  Control plane gets the small flowset every 10ms
We implemented it using P4 Language.

## Slide 12: FlowRadar architecture
Flow&counter
Correlate network wide info to extract per-flow counter
Analyze
Each switch maintains a fast and efficient data structure for half-baked per-flow counter
Collector
Network
Periodic report
Encoded flowset
Encoded flowset
Encoded flowset
Stage1.SingleDecode
Stage2. Network-wide Decode
FlowXor | …
FlowCount | …
PacketCount | …
Bloom filter
Counting table
Flow filter

## Slide 13: Stage1. SingleDecode
FlowXor | …
FlowCount | …
PacketCount | …
Bloom filter
Counting table
Flow filter
Flow | #packet
a | S(a)
… | …
Input: a single encoded flowset
Output: per-flow counters

## Slide 14: Stage1. SingleDecode
Flow | #packet
a | 5
FlowXor | a | a⊕b | b⊕c⊕d | b⊕c⊕d | a | c⊕d
FlowCount | 1 | 2 | 3 | 3 | 1 | 2
PacketCount | 5 | 12 | 13 | 13 | 5 | 6
Flow filter
Find a pure cell: a cell with one flow
Remove the flow from all cells
Pure cell
Decoded:
-1
-1
-1
-5
-5
-5

## Slide 15: Stage1. SingleDecode
FlowXor | 0 | b | b⊕c⊕d | b⊕c⊕d | 0 | c⊕d
FlowCount | 0 | 1 | 3 | 3 | 0 | 2
PacketCount | 0 | 7 | 13 | 13 | 0 | 6
Flow filter
Find a cell with one flow (pure cell)
Remove the flow from all cells
  Create more pure cells
Iterate until no pure cells
Flow | #packet
a | 5
Decoded:

## Slide 16: Stage1. SingleDecode
FlowXor | 0 | 0 | c⊕d | c⊕d | 0 | c⊕d
FlowCount | 0 | 0 | 2 | 2 | 0 | 2
PacketCount | 0 | 0 | 6 | 6 | 0 | 6
Flow filter
Flow | #packet
a | 5
b | 7
Decoded:
We want to leverage the network-wide info
to decode more flows

## Slide 17: FlowRadar architecture
Analyze
Flow&counter
Collector
Network
Stage1.SingleDecode
Stage2. Network-wide Decode
Periodic report
Encoded flowset
Encoded flowset
Encoded flowset

## Slide 18: Key insight: overlapping sets of flows
The sets of flows overlap across hops
  We can use the redundancy to decode more flows
Use different hash functions across hops
a
b
c
d
a
b
c
d
a | a⊕c ⊕d | b⊕c ⊕d | a⊕b ⊕c | b⊕d
1 | 3 | 3 | 3 | 2
a⊕d | a⊕c | b⊕c ⊕d | a⊕b ⊕c | b⊕d
2 | 2 | 3 | 3 | 2
FlowXor
FlowCount
PktCount
FlowXor
FlowCount
PktCount
Use 5 cells to decode 4 flows
10
Collector can leverage flowsets from all switches to decode more
    Provision memory based on avg(#flows), not max(#flows)
    SingleDecode for normal case
    Network-wide decoding for bursts of flows

## Slide 19: Challenge 1: sets of flows not fully overlapped
Flows from one switch may go to different next hops
One switch receive flow from multiple hops
a
b
c
d
a
e
c
d

## Slide 20: Challenge 1 solution: use flow filter to check
Generalize to network
  No need for routing info
  Incremental deployment
Flow filter
Flow filter
a
a
b
c
d
Decoded:
a
e
c
d
a
b
c
c
d
d
e
SingleDecode
SingleDecode
Remove from the other

## Slide 21: Challenge 2: counters are different across hops
The counter of a flow may be different across hops
  Some packets may get lost
  On-the-fly packets
drop

## Slide 22: Challenge 2 solution: solve linear equations
We got full list of flows
Combine with counting table
Construct and solve a linear equation system for each switch
Speed up by using counter’s properties to stop solver earlier
a
b
c
d
…
…
…
FlowXor
FlowCount
PktCount
Flow | #pkt
a | 5
b | 7
c | 4
d | 2

## Slide 23: FlowRadar architecture
Analyze
Flow&counter
Collector
Network
Stage1.SingleDecode
Stage2. Network-wide Decode
Stage2.1 FlowDecode
Stage2.2 CounterDecode
Periodic report
Encoded flowset
Encoded flowset
Encoded flowset

## Slide 24: Evaluations
Analyze
Flow&counter
Collector
Network
Stage1.SingleDecode
Stage2.1 FlowDecode
Stage2.2 CounterDecode
Periodic report
Encoded flowset
Encoded flowset
Encoded flowset
Memory efficiency
Bandwidth usage
SingleDecode vs. Network-wide Decode

## Slide 25: Evaluation
Simulation of k=8 FatTree (80 switches, 128 hosts) in ns3
Config the memory base on avg(#flow),
  when burst of flows happens, use network-wide decode
The worst case is all switches are pushed to max(#flow)
  Traffic: each switch has same number of flows, and thus same memory
Each switch reports the flowset every 10 ms.

## Slide 26: Memory efficiency
#cell=#flow
(Impractical)
FlowRadar: 2.36MB
FlowRadar: 24.8MB
Log scale

## Slide 27: Other results
Bandwidth usage
  Only 0.52% based on topology and traffic of Facebook data centers (sigcomm’15)
NetDecode improvement over SingleDecode
  SingleDecode 100K flow, which takes 10ms
  NetDecode 26.8% more flows with the same memory,
  which takes around 3 sec

## Slide 28: FlowRadar analyzer
Analyze
Flow&counter
Collector
Network
Stage1.SingleDecode
Stage2. Network-wide Decode
Periodic report
Encoded flowset
Encoded flowset
Encoded flowset

## Slide 29: Analysis applications
Flow coverage
  Transient loop/blackhole
  Error in match-action table
  Fine-grained traffic analysis
Temporal coverage
  Short time-scale per-flow loss rate
  ECMP load imbalance
  Timely attack detection

## Slide 30: Per-flow loss map: better temporal coverage
Detect loss faster than NetFlow
Chart: 
 | 0 | 5 | 5 | 5 | 0 | 0 | 5 | 5 | 5 | 5 | 0
Chart: 
 | 0 | 5 | 4 | 5 | 0 | 0 | 5 | 5 | 5 | 5 | 0
Switch 1
Switch 2
15 packets
14 packets
35 packets
34 packets
NetFlow
detects loss
FlowRadar
detects loss

## Slide 31: Conclusion
Report counters for all flows in fine-grained time granularity
Fully leverage the capability of both the switches and the collector
  Switch: fixed per-packet processing time, memory-efficient
  Collector: Network-wide decoding
FlowRadar
Overhead at
the collector
Overhead at the switches
NetFlow
Mirroring