## Slide 1: LossRadar: Fast Detection of Lost Packets in Data Centers
Yuliang Li
Rui Miao Changhoon Kim Minlan Yu

## Slide 2: Packet loss diagnosis is important
Losses are common because of the large scale
  40-80 machines see 50% packet loss [Jeff Dean’s talk from Google]
  Network maintenance jobs cause 30-minute random connectivity losses [Jeff Dean’s talk from Google]
  One to ten new switch blackholes every day [Microsoft]
Losses have high impact
  High latency, low throughput
  Break connection

## Slide 3
I fail to connect!
Me too!
Counters
Where?
Hard to locate
Not generic
Problems:

## Slide 4
4
Where?
S1
S2
S3
S4
S5
S6
…
…
…
Large overhead
Hard to locate
Not generic
Problems:

## Slide 5
5
Why?
Where?
Large overhead
Hard to locate
Not generic
Problems:
Unknown root cause
Time consuming
Congestion?
Blackhole?
Random drops?
    Detect losses
    Fast
    With location info.
    Generic to all types of losses
    Low overhead
    Diagnose losses
    Root causes

## Slide 6: Challenge: diversity of loss types
OutputPort 1
Output Port n
Input Port 1
Input Port n
Input buffer
…
parser
Ingress match-actions
(L2->L3->ACL)
Shared buffer
Egress match-actions
…
Switch CPU
Configure
Rule
corruptions
mis-config
updates
Resource shortage
Resource shortage
Packet corruptions
Grey failure
Rule corruptions
mis-config
updates
Takeaway:
Need to be generic to all types

## Slide 7: Challenge: diagnose root causes
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
congestion
blackhole
Random drop
Takeaway:
Need the information of individual losses

## Slide 8: LossRadar overview
Knowing location  Install meters to monitor traffic
Fast detection  Frequently send traffic digest to collector
Being generic  Compare packets across hops
Need info of individual losses  Include details of each loss
Low overhead ?
Digest Collector
Traffic Digest
Traffic Digest
Traffic Digest

## Slide 9: Storing all packets is too heavy
Collector
Switches

## Slide 10: Storing all packets is too heavy
Capture: O(#loss)
Memory: O(#packet)
= 10-5~10-4
Collector
Switches

## Slide 11: Solution: put all packets in a small memory
View the problem as set difference
  Can be solved using O(#loss) memory
  Unique packet ID = <5-tuple, IP_Identification>
Mix all packets in the small memory at each switch
Collector subtracts two sets, same packets cancel out

## Slide 12: Invertible Bloom Filter: multiple hashes
H1
xorSum count |  |  |  |  | 
a
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
a = <5-tuple, IP_Identification >

## Slide 13: Invertible Bloom Filter: multiple hashes
H1
xorSum count | a 1 |  | a 1 | a 1 | 
a
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
a = <5-tuple, IP_Identification >

## Slide 14: Invertible Bloom Filter: mix packets with XOR
H1
xorSum count | a 1 |  | a 1 | a 1 | 
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
b

## Slide 15: Invertible Bloom Filter: mix packets with XOR
H1
xorSum count | a 1 | b 1 | a⊕b 2 | a 1 | b 2
H2
H3
[Invertible Bloom Filter (Sigcomm’ 11)]
b

## Slide 16: Same hash functions across switches
xorSum count | 0 0 | 0 0 | 0 0 | 0 0 | 0 0
xorSum count | 0 0 | 0 0 | 0 0 | 0 0 | 0 0
upstream
downstream
Collector
[Invertible Bloom Filter (Sigcomm’ 11)]

## Slide 17: Same hash functions across switches
a
a
a
xorSum count | a 1 | 0 0 | a 1 | a 1 | 0 0
xorSum count | 0 0 | 0 0 | 0 0 | 0 0 | 0 0
upstream
downstream
Collector
a
drop
[Invertible Bloom Filter (Sigcomm’ 11)]

## Slide 18: Same hash functions across switches
b
b
b
xorSum count | a 1 | b 1 | a⊕b 2 | a 1 | b 1
xorSum count | 0 0 | b 1 | b 1 | 0 0 | b 1
a
a
a
upstream
downstream
Collector
b
b
b
b
b
[Invertible Bloom Filter (Sigcomm’ 11)]

## Slide 19: Same hash functions across switches
c
c
c
upstream
downstream
Collector
xorSum count | a⊕c 2 | b⊕c 2 | a⊕b 2 | a⊕c 2 | b 1
xorSum count | 0 0 | b 1 | b 1 | 0 0 | b 1
b
b
b
a
a
a
b
b
b
c
drop
[Invertible Bloom Filter (Sigcomm’ 11)]

## Slide 20: Same hash functions across switches
d
d
d
upstream
downstream
Collector
xorSum count | a⊕c⊕d 3 | b⊕c 2 | a⊕b⊕d 3 | a⊕c 2 | b⊕d 2
xorSum count | d 1 | b 1 | b⊕d 2 | 0 0 | b⊕d 2
c
c
c
b
b
b
a
a
a
b
b
b
d
d
d
d
d
xorSum count | a⊕c 2 | c 1 | a 1 | a⊕c 2 | 0 0
c
a
a
a
c
c
Collector does
subtraction
[Invertible Bloom Filter (Sigcomm’ 11)]

## Slide 21: Retrieve losses
xorSum count | a⊕c 2 | c 1 | a 1 | a⊕c 2 | 0 0
c
a
a
a
c
c
Collector

## Slide 22: Retrieve losses
xorSum count | a⊕c 2 | c 1 | a 1 | a⊕c 2 | 0 0
c
a
a
a
c
c
Loss:
-1
-1
-1
c
Collector

## Slide 23: Retrieve losses
xorSum count | a 1 | 0 0 | a 1 | a 1 | 0 0
a
a
a
a
Loss:
c
-1
-1
-1
Collector
Only need O(#loss) memory

## Slide 24: Benefits
Memory-efficient
Report a batch of packets every 10 ms
  ~10Mbps for 10Gbps traffic (including incast, blackhole and random drops)
Extend to collect more packet information
  TTL: help identify loops
  Timestamp
  Any other fields that programmable switches can configure
Easy to implement in P4

## Slide 25: Challenge: batch alignment
Ideally
In fact
upstream
downstream

## Slide 26: Solution: packets carry batch ID
Just need 1 bit to distinguish adjacent batches
0
0
0
0
0
0
0
1
1
1
1
upstream
downstream

## Slide 27: Need to cover the whole network
meter
meter
meter
meter
meter

## Slide 28: Solution: pair-wise deployment
Cover all pipelines
UM
DM
UM
DM
Cover ingress pipeline
Cover egress pipeline
UM: Upstream meter
DM: Downstream meter
UM
DM
UM
DM
Ingress pipeline
shared
buffer
Egress pipeline
DM
UM
DM
UM

## Slide 29: Challenge: incremental deployment
Compare sum(UMi) and sum(DMi)
Blackbox
UM
DM
UM
DM
LossRadar
LossRadar
UM
DM
LossRadar
LossRadar
UM
DM

## Slide 30: LossRadar overview
Fast detection
Knowing location
Include details of each loss
Being generic
Low overhead
Digest Collector
Traffic Digest
Traffic Digest
Traffic Digest

## Slide 31: Root cause inference
Digest Collector
Traffic Digest
Traffic Digest
Traffic Digest
Root cause inference

## Slide 32: Root cause inference
Different root causes have different loss patterns
  Temporal: how the losses distribute over time
  Inter-flow: specific set of flows? All flows?
  Intra-flow: which packets of a flow?

## Slide 33: Root cause inference
Different root causes have different loss patterns
  Temporal: how the losses distribute over time
  Inter-flow: specific set of flows? All flows?
  Intra-flow: which packets of a flow?
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Time (us)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
Dst IP = 10.0.0.0/24

## Slide 34: Root cause inference
Different root causes have different loss patterns
  Temporal: how the losses distribute over time
  Inter-flow: specific set of flows? All flows?
  Intra-flow: which packets of a flow?
 | Temporal | Inter-flow | Intra-flow
Congestion | Bursty | All flows on an egress port | Non-deterministic
Blackhole | Bursty / non-bursty | Specific flows | Consecutive
Random drops | Non-bursty | All flows | Non-deterministic
LossRadar
Timestamp
5-tuple
IP_ID
 | Temporal | Inter-flow | Intra-flow
Congestion | Bursty | All flows on an egress port | Non-deterministic
Blackhole | Bursty / non-bursty | Specific flows | Consecutive
 | Temporal | Inter-flow | Intra-flow
Congestion | Bursty | All flows on an egress port | Non-deterministic

## Slide 35: LossRadar evaluation
Simulation of k=8 FatTree in ns3
  80 switches, 128 hosts, 10G links
Send traffic according to the pattern in DCTCP
Inject different types of losses
  Incast
  Blackholes
  random drops
Each switch reports the traffic digest every 10 ms.

## Slide 36: Low memory usage

## Slide 37: Compare with state-of-the-art solutions
LossRadar vs. full mirroring
  0.5% bandwidth compared to NetSight with batch compression
LossRadar vs. per-flow counter
  1.4% memory compared to FlowRadar

## Slide 38: High inference accuracy across all types

## Slide 39: Conclusion
Loss diagnosis is very important
  High impact on performance
  Diagnosis takes a lot of human effort
LossRadar can detect losses and diagnose root causes
  Detection: details of individual losses, with locations, within 10ms
  Diagnosis: correctly discover root causes
P4 code: https://github.com/liyuliang001/LossRadar-P4