## Slide 1
HPCC: High Precision Congestion Control
Yuliang Li
Rui Miao, Hongqiang Harry Liu, Yan Zhuang, Fei Feng, Lingbo Tang, Zheng Cao, Ming Zhang, Frank Kelly, Mohammad Alizadeh, Minlan Yu
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3

## Slide 2: High-performance networking is desired
High-performance storage
HDDSSDNVMe
Higher-throughput, lower latency
1M IOPS / 50~100us
CPUGPU, FPGA, ASIC
Faster compute, lower latency
E.g. latency <10us
Distributed deep learning
More network load
Need ultra-lower latency: 3-5us
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3
Resource disaggregation
compute
compute
compute
storage
storage
Network IO
network
C
C
C
M
M
M
G
G
G
M

## Slide 3: Two essential steps to high performance
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3
Network
App
Stack
NIC
App
Stack
NIC
App
Stack
NIC
Many ongoing efforts on hardware offloading
- RDMA, SmartNIC
More severe congestion
So Congestion control (CC) is very important!
CC
CC
CC

## Slide 4: CC is immature in high-speed network
State-of-the-art CC in hardware-offloading solutions
  DCQCN[SIGCOMM 15]: ECN-based
  TIMELY[SIGCOMM 15]: delay-based
Face problems in operating large-scale RDMA networks
Root cause is the CC

## Slide 5: Problems of state-of-the-art
Stability issues: incast/failure cause PFC storms or deadlock
Slow convergence
Challenge in reconciling BW-hungry app and latency-sensitive app
Standing queue
Parameter tuning takes months
CC parameters is hard to tune

## Slide 6: Problem 1: slow convergence
Operators’ problem
  Buffer overflow happens during incast/failure
    Use PFC to prevent loss: good performance on average, threat from PFC storm and deadlock
    Disable PFC: bad performance on average.
Root cause: CC cannot control the buffer well, because of slow convergence
  Imprecise feedback (ECN, delay) cannot tell the rate mismatch
  CC resolves congestion slowly, by halving the rate per RTT
  More severe in higher speed networks, because filling buffer faster
Ideally, adjust to the right rate in one RTT
  So loss is rare, and do not need PFC

## Slide 7: Problem 2: standing queues
Operators’ problem:
  Hard to run BW-hungry app and latency-sensitive app in the same cluster
Network
~5us base RTT
ML
ML
ML
Storage
Storage
>100µs latency

## Slide 8: Problem 2: standing queues
Root cause is CC
Feedback (ECN/delay) relies on the queue
CC intentionally keeps standing queues
Add 20~50us queueing delay
4~10x base RTT!!!

## Slide 9: Problem 3: complex parameter tuning
Tradeoffs
Many factors affect the tradeoffs
  Traffic patterns, failure scenarios, and network arch
Feedback (ECN/delay) is imprecise
  CC has to use heuristics to guess (1) network condition; (2) rate adjustments
Many parameters in such heuristics
  e.g., 15 parameters in DCQCN
  Tuning takes several months
Utilization
Stability
Throughput
Latency

## Slide 10: Problems of state-of-the-art
Slow convergence
No precise feedback indicating how much to increase/decrease
Standing queue
Feedback relies on queue
Complex parameter tuning
No precise feedback  need heuristics: lots of parameters
One fundamental issue: coarse-grained feedback
What if we have precise feedback?

## Slide 11: HPCC: use INT as precise feedback
In-band network telemetry (INT) provides many details per packet
Broadcom&Barefoot have INT in recent products.
Widely used for diagnosis and monitoring in production
pkt
pkt
pkt
INT
INT
Sender
Receiver
Link-1
Link-2

## Slide 12
How good can CC do with INT as the feedback?
We design HPCC to answer this question

## Slide 13: HPCC solves the 3 problems
Slow convergence
No precise feedback indicating how much to increase/decrease
Standing queue
Feedback relies on queue
Complex parameter tuning
No precise feedback  need heuristics: lots of parameters
One fundamental issue: coarse-grained feedback
Using INT as the precise feedback
Fast convergence
Sender knows the precise rate to adjust to, on every ACK
Near-zero queue
Feedback does not rely on queue
Few parameters
Precise feedback, so no need for heuristics which requires many parameters

## Slide 14: HPCC: overview and challenges
ACK
Adjust rate
per ACK
Challenge 1: Feedback delay:
- Pkt/ACK may gets delayed
Challenge 2: Overreaction:
- Diff ACKs bring overlapping feedback
pkt
pkt
pkt
INT
INT
Sender
Receiver
Link-1
Link-2

## Slide 15: Challenge 1: tolerate feedback delay
feedback
T
0
2T
Rate (DCQCN/TIMELY)
feedback
T
0
2T
No congestion
Congestion
High rate persists
Can be >> T
Because T is very low and
queueing delay dominates
(T is the base RTT )
HPCC
feedback
T
0
2T
Each sender use a window to limit inflight bytes: W=target_rate×T

## Slide 16: Challenge 1: tolerate feedback delay
feedback
T
0
2T
Congestion
feedback
T
0
2T
Need a new way of measuring congestion:
Rate-based scheme
Use rate mismatch
HPCC
Rate mismatch is bad measurement
Actual sending rate is non-constant, due to the inflight bytes limit

## Slide 17: Estimating inflight bytes
Use total inflight bytes to measure congestion
  Each flow needs to estimate the total inflight bytes
  Use INT to estimate the total inflight bytes
sender
B (bottleneck bandwidth)
T (base RTT)
Queue
congestion
No
Each sender estimates independently in a distributed way
Available in INT

## Slide 18: Controlling inflight bytes
Use total inflight bytes to measure congestion
  Each flow needs to estimate the total inflight bytes
  Use INT to estimate the total inflight bytes
Compute adjustment based inflight bytes
  Use MIMD to quickly adjust to the right rate

## Slide 19: Challenge 2: Fast reaction without overreaction
3
4
2
1
5
W=W0
/1.5
Ack1
Pipe volume=6
Per-ACK reaction
Overreaction

## Slide 20: Challenge 2: Fast reaction without overreaction
3
4
5
W=W0
/1.5
Ack1
Pipe volume=6
2
/1.3
Ack2
Overlap
overreaction
Per-ACK reaction
Overreaction

## Slide 21: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Per-RTT reaction
No overreaction
3
4
2
1
5
W=W0
/1.5
Ack1
Pipe volume=6
6
Next to react: 6

## Slide 22: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Per-RTT reaction
No overreaction
6
W=W0
/1.5
Ack1
Pipe volume=6
/1.1
Ack6
No overlap
no overreaction
Next to react: 6

## Slide 23: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Fast reaction to sudden bursts
Per-RTT reaction
No overreaction
Miss sudden bursts
W=W0
/1.5
Ack1
3
4
2
1
5
Pipe volume=6

## Slide 24: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Fast reaction to sudden bursts
Per-RTT reaction
No overreaction
Miss sudden bursts
HPCC combines per-ACK and per-RTT (details in paper)
No overreaction
Fast reaction to sudden bursts

## Slide 25: Theory proof
Asynchronized flows
Arbitrary topology
Convergence speed
Queueing delay
Fairness
Converge to Pareto optimal
Queue size is bounded
Max-min/proportional fairness

## Slide 26: Implementation
Commodity FPGA NIC
In a 32-server testbed

## Slide 27: Implementation in commodity FPGA NIC
14,000 lines of Verilog code for the whole NIC
2,000 lines for CC
  <2% of hardware resources
Optimization:
  look-up table: 8x speedup for division
  h/w friendly compression with <1% error: 10KB for [1, 4M]
  Multiple parallel engines: 6x more concurrent flows
INT header overhead: 4.2% (MTU=1KB)

## Slide 28: Implementation: testbed
Each server has two 25G FPGA NICs
32 servers

## Slide 29: Evaluations
Setup
  32-server, 5-switch Testbed (25GE)
  320-server, 56-switch simulation, (100GE)
Traffic setting
  Web search, with diff levels of traffic load
  Hadoop, with diff levels of traffic load
  Diff incast sizes & ratios
  Many micro-benchmarks
Compare with DCQCN, TIMELY, DCTCP, with their recommended parameters
Metrics
  Flow completion time (FCT)
  Queue length distribution

## Slide 30: HPCC achieves lower FCT and near-zero queue
In testbed, vs. DCQCN (hardware-based, widely used in industry)
  Web search traffic at 50% load
Vs. other CC (unavailable in HW) in simulation. HPCC performs better
95% lower
55% lower
HPCC
- P99: 23KB (7us queue delay)

## Slide 31: HPCC has the potential to remove PFC
HPCC is persistently better, regardless of the flow control schemes
HPCC is insensitive to the flow control schemes
95 percentile FCT

## Slide 32: Conclusion
Collaborating with switch and NIC partners on
deploying HPCC in Alibaba’s production networks
Practical impact
Demonstrate problems of existing CC with real production experience
Implement HPCC with HW NIC & switch
Demonstrate using precise info from INT make CC highly performant
Address the challenge of using INT
Proof for convergence speed, queueing delay, and fairness
Advance in CC